## Slide 1: Multi-Task Learning for Location Estimation Using RSSI of Wireless LAN in NLoS Environment TeleAILab 2022-Dec-01
Notes: Multi-task learning
Rising

## Slide 2: Background
  Outdoor location recognition Indoor location estimation
  People tracking in shopping malls, robot localization, autonomous car parking…
Credit to: http://www.hkzbai.com/show-10-51-1.html
Credit to: https://baike.baidu.com/pic/全球定位系统/1240960
Line of Sight (LoS)
Non Line of Sight (NLoS)
Notes: Global Navigation Satellite System (GNSS) requires a direct LOS and the connection to at least 4 satellites simultaneously. It has a large position error and blocks signals on buildings and walls for indoor environment.
Non-line of sight (NLOS) refers to the path of propagation of a radio frequency (RF) that is obscured (partially or completely) by obstacles
Terminalogy: LoS/Nlos APs RSSI/RFID/Bluetooth have been studied for indoor location recognition.
Indoor location-based service is promising, such as smart retail

## Slide 3: Problem description
  Received Signal Strength Indication (RSSI) refers to access point (AP)
  LoS/NLoS environment
Notes: - 4 access points
Points with RSSI from corresponding Aps
Latitude & longitude
To estimate latitude and longitude for verification points with given RSSI

## Slide 4: Motivation
Triangulation/Trilateration
Fingerprint
  RSSI is inversely proportional to the distance to the power of a path loss exponent.
  Wi-Fi fingerprinting is usually conducted in two phases: an offline survey and an online query.
Credit to: Ilci et al. “Trilateration Technique for WiFi-Based Indoor Localization”
Credit to: Lee et al. “Random forest and WiFi fingerprint‐based indoor location recognition system using smart watch
”
Credit to: Khokhar et al. “Machine Learning-Based Indoor Localization using Wi-Fi and Smartphone”
Credit to: He et al. “Wi-Fi Fingerprint-Based Indoor Positioning:
Recent Advances and Comparisons
”
Notes: Recently, fingerprint-based methods drawn lots of attentions.
Green -> blue

## Slide 5: Motivation
Triangulation/Trilateration
Fingerprint
  RSSI is inversely proportional to the distance to the power of a path loss exponent.
  Wi-Fi fingerprinting is usually conducted in two phases: an offline survey and an online query.
Credit to: Ilci et al. “Trilateration Technique for WiFi-Based Indoor Localization”
Credit to: Lee et al. “Random forest and WiFi fingerprint‐based indoor location recognition system using smart watch
”
Credit to: Khokhar et al. “Machine Learning-Based Indoor Localization using Wi-Fi and Smartphone”
Credit to: He et al. “Wi-Fi Fingerprint-Based Indoor Positioning:
Recent Advances and Comparisons
”
Notes: Recently, fingerprint-based methods drawn lots of attentions.
Green -> blue

## Slide 6: Historical methodology
  RSSI is inversely proportional to the distance to the power of a path loss exponent.
Lognormal model
Frii’s formula
FSPL
, and
Notes: Theoretical studies on RSSI-distance relationships
LOS/NLOS can be considered through a bias term
Historical analysis/methodology

## Slide 7: Our Solution
  Our solution includes of three key steps.
Data Processing Location Estimation Evaluation
Modeling
Statistics
Mean error (m)
Maximum error (m)
Processing
v.s.
Notes: Modeling separasion.
MTL network visulization and introduction
re-orgnize

## Slide 8: Our Solution – Data Processing
  The distribution of the verification data resembles the one of the training data.
  The RSSI strength is linear to the
Notes: Investigate RSSI-distance relations

## Slide 9: Our Solution – Data Processing
  No. offers little information, Channel contains constant values.
  There are duplicated samples, and little fluctuation with time.
Notes: Channel: constant, remove
Positional information
LOS/NLOS
Temporal information is useless

## Slide 10: Our Solution – Data Processing
  Augment data by permute the order the APs.
Notes: Ways of data augmentation.

## Slide 11
Our Solution – Location Estimation – Tree models
XGBoost
Random Forest
Extra Tree Regression
Latitude
Longitude
  Two models are necessary to predict latitude and longitude, respectively.
Notes: Two models to predict latitude and longitude, individually.

## Slide 12
Our Solution – Location Estimation – Multi-task learning
Input
Shared
Tower
Lat
Tower
Lon
Latitude estimation
Longitude estimation
RSSI
Distance
Latitude
Longitude
Trilateration/Triangulation
Predict latitude and longitude
in one model
Explanation:
…
…
…
…
…
Notes: One model to predict the position.
Stein’s paradox: estimating the means of three or more Gaussian random variables using samples from all of them could yield better performance than estimating them separately
Model interpretation

## Slide 13: Our Solution – Results
  Multi-task learning model obtains the best mean error.
  Most predictions of the multi-task learning model are relatively good.
error
Count
Notes: 直方图形式
还需要另加多任务优化图

## Slide 14: Our Solution – Results
Notes: 直方图形式
还需要另加多任务优化图
Conclusion: augmentation + mtl (mining)

## Slide 15: Outlook
Explicit usage of LoS/NLoS information
Spatial dependencies
Dynamics
6G
Notes: Conclusion + outlook
6G application/ emphasize application value

## Slide 16: Thank you!

## Slide 17
…
Input
…
Shared
Tower lat
Tower lon
Latitude estimation
Latitude estimation